## Slide 1: Basic Theory of Motion Profiling in Code
ThunderChickens – FRC Team 217

## Slide 2: Types of Profiles
Ramp rate
Geometric
  Purely geometric
  Geometric with PID
Waypoint (trajectories)

## Slide 3: Ramp Rate
Add to the velocity at a given rate
, or
  is target acceleration
  We typically work in deltas (, )
Used in combination with position PID
  Setpoint is final position, measurement is current position
  Hand control of velocity over to PID once the ramp rate and PID lines intersect ()

## Slide 4: Ramp Rate
Pros:
  Easy to write
  Easy to use
  Motors don’t start at full speed
Cons:
  Can’t apply on the deceleration period
    Causes overshoot
  Still has all the issues of traditional position PID after reaching full speed

## Slide 5: Ramp Rate – alternate formula
Assume v is a parameter that does not exceed the max velocity of the motor controller
  is current acceleration
  returns +1 if input is positive, -1 if negative, 0 if zero
  Only runs if and if (speeding up)
Logic
  Need to get the sign of a since is used, and is positive
  , accelerating too fast, subtracts the error in from

## Slide 6: Geometric – Purely Geometric
Velocity vs Time graph forms a trapezoid
Given target distance, max velocity, and target acceleration, can calculate how long to accelerate and decelerate, and how long to drive full speed in between
Area under graph is position:
Slope of graph is acceleration:

## Slide 7: Geometric – Purely Geometric
Pros:
  Doesn’t rely on encoders
Cons:
  Relies on a perfect system
  More complicated to calculate than ramp rate, but less effective
No good team utilizes this system

## Slide 8: Geometric – With PID
Take the Purely Geometric curve
Using integrals, calculate target velocity and target position at a given time
Using velocity control mode:
  motor.set(ControlMode.Velocity, vt + pid.getOutput(p, pt))
    vt is target velocity (from profile)
    p is current position
    pt is target position (from profile)
  Configure kF (feed forward) on the motor controller
    Get motor velocity (with load) at a given percent output (Recommended: ~75% of max)
    For CTRE:

## Slide 9: Geometric – With PID
Pros:
  Precise
  Applies to both acceleration and deceleration
  Manages errors in position and velocity
Cons:
  Harder to program

## Slide 10: Waypoint (trajectories)
Calculate multiple points along a path, their position, and the target velocity at those points using a Hermite spline
Same calculations as a Geometric controller with PID

## Slide 11: Waypoint (trajectories)
Pros:
  Very precise
  Provides tremendous control over motion
  Allows for curved trajectories
Cons:
  Very difficult to program, use pre-made libraries/applications to calculate paths
  Excessive for linear trajectories

## Slide 12: When to Use Which
Ramp rate
  Want to use standard position PID control (if it ain’t broke, don’t fix it)
  Need to control acceleration and/or jerk in teleop
Purely Geometric
  Just…don’t
Geometric with PID
  Want to have precise control of linear trajectories or of a single robot component (elevator, arm, etc.)
Waypoint
  Want to accurately move along curved trajectories (drivebase)

## Slide 13: What We’re Using
Pre-2020: Pure PID
  High current draw from motors
  Wheelies at start and (sometimes) end of motion
2020: Ramp rates
  Pure PID, except we control the speedup period
  Significantly lower current draw
  Wheelies (sometimes) at end of motion
2021 Goal: Geometric with PID
  Smooth, precise control both speeding up and slowing down
  Lowest current draw
  No wheelies
2021: Investigate Waypoints
  Allows for curved trajectories instead of “drive straight then turn”